## Slide 1
DIGITAL LOGIC DESIGN
Design and Simulation of a 4-Bit Binary-to-Decimal Conversion and Display System
01
NAME:SANJAY KILARI ROLLNO:2620030215
NAME :SRI DEEKSHITH ROLLNO:2620030285
NAME:D. VISHNU SAI ROLLNO:2620030306
NAME: M.CHARAN TEJ ROLLNO:2620030291
GROUP:2

## Slide 2
INTRODUCTION
02
From Binary Bits to a Visible Digit
Background • domain overview • importance
WHAT IS THE PROJECT?
A 4-bit binary input is converted into its corresponding decimal value from 0 to 9 and then represented on a 7-segment display.
DIGITAL LOGIC DOMAIN
The system uses combinational logic, Boolean expressions, NOT gates, AND gates, decoding stages, and 7-segment segment control.
WHY IT MATTERS
It demonstrates how digital systems translate encoded binary information into a human-readable decimal output and provides a practical simulation exercise.
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 3
PROBLEM STATEMENT
03
Problem Statement
Why a decoding stage is needed
THE CHALLENGE
A 4-bit input can represent 16 combinations (0000–1111), but the required display system is designed for decimal digits 0–9. A circuit is therefore needed to identify each valid binary pattern and activate the correct decimal output.
LIMITATION
Inputs 1010–1111 do not correspond to the required decimal digit range 0–9.
NEED FOR THE PROJECT
A structured decoder provides one active decimal line for each valid input and enables the selected value to drive the 7-segment display reliably.
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 4
OBJECTIVES
04
Objectives
Specific goals of the design and simulation
01
Design a 4-to-10 binary-to-decimal decoder.
02
Implement Boolean logic using NOT and AND gates.
03
Connect decimal outputs to a 7-segment decoding stage.
04
Simulate all valid inputs from 0000 to 1001.
05
Observe and verify the displayed decimal digit.
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 5
LITERATURE SURVEY / EXISTING SYSTEM
05
Existing Approaches & Their Limitations
BOOLEAN DECODERS
Combinational decoder designs use Boolean expressions and logic gates to activate one output for each input combination.
DECIMAL DECODING
A 4-to-10 decoder is suitable for representing decimal digits 0–9 from a 4-bit binary input.
DISPLAY STAGE
A 7-segment decoder converts the selected decimal value into segment-control signals. Basic designs need explicit handling for invalid inputs.
Design insight: separate the problem into decoding and display stages for easier verification.
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 6
PROPOSED SYSTEM
06
Proposed System
A modular decoder-to-display pipeline
4-BIT INPUT
B3 B2 B1 B0
→
4-TO-10 DECODER
D0 … D9
→
10-TO-7 DECODER
a b c d e f g
→
7-SEGMENT
DIGIT 0–9
KEY FEATURE
Exactly one decimal output is active for each valid input.
IMPROVEMENT
Simple modular stages make the design easier to simulate and verify.
VALID RANGE
0000–1001 → decimal 0–9.
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 7
METHODOLOGY / IMPLEMENTATION
07
Methodology & Implementation
Design steps • components • working principle
01
INPUT
Provide B3, B2, B1, B0.
02
INVERT
Generate complemented inputs with NOT gates.
03
DECODE
Build D0–D9 using 4-input AND gates.
04
DISPLAY
Feed the selected decimal line into the 7-segment stage.
05
VERIFY
Test valid inputs and observe the displayed digit.
CORE BOOLEAN LOGIC
D0 = ¬B3 · ¬B2 · ¬B1 · ¬B0 D1 = ¬B3 · ¬B2 · ¬B1 · B0
D2 = ¬B3 · ¬B2 · B1 · ¬B0 D3 = ¬B3 · ¬B2 · B1 · B0 D9 = B3 · ¬B2 · ¬B1 · B0
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 8
RESULTS & DISCUSSION
08
Results & Discussion
Truth table + representative simulation cases
VALID INPUTS
B3 B2 B1 B0
DEC
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
1000
8
1001
9
TEST 1
0000 → 0
TEST 2
0101 → 5
TEST 3
1000 → 8
TEST 4
1001 → 9
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 9
CONCLUSION
09
Conclusion
Project achievements and objective fulfillment
ACHIEVEMENTS
✓ 4-bit input decoded into decimal values 0–9. ✓ NOT and AND gates provide the required combinational logic. ✓ 7-segment decoding produces the corresponding visible digit. ✓ Simulation confirms expected results for valid inputs.
FUTURE IMPROVEMENT
Handle inputs 1010–1111 as blank / invalid states. The modular design can also be extended with additional display logic or input/output interfaces.
OBJECTIVE → DESIGN → SIMULATION → VERIFICATION
4-Bit Binary-to-Decimal Conversion & Display System
Logisim • Combinational Logic

## Slide 10
THANK YOU
Questions & Discussion
Design and Simulation of a 4-Bit Binary-to-Decimal Conversion and Display System